Design Note
&
Installation Guide

The ADC Driver

T Karuantiallake
September 2011

Introduction

A Linux driver is required to capture and provide Analogue to Digital conversion results into the user space for up to 8 analogue channels connected to the microprocessor via the ADC Touchscreen Controller on the board. This document details the design of the insync_adcc.ko driver programmed as a kernel loadable modules, the instructions on how to build and install the driver, and the design of the development and test tools to facilitate user-space development and testing of the controller using the driver.

Design
Figure 1: The TSADCC Controller and its pins.

The Input Pins

The analogue inputs (up to 8) are to be connected to the input pins AD0, AD1, AD2, AG3, GPAD4, GPAD5, GPAD6, GPAD7. Software ID's 0-7 are assigned to these pins respectively.

Currently not all inputs are used in every product. The pin usage is defined in file AT91SAM9G45_pinout.py as detailed in Figure 2.

Driver Pin ID	Pin	Signal Name	Periph A	A Desc	IQP Use	HDS Use	FRC Use
7	H2	PD27	PCK1	Sys Contr/GPAD7	PSUB		NSW_MON
6	H1	PD26	PCK0	Sys Contr/GPAD6	PSUA		NSW_DWN
5	G1	PD25	SPIO_NPCS2	SPI0/GPAD5	BLDM2		NSW_UP
4	F2	PD24	SPIO_NPCS1	SPI0/GPAD4	BLDM1		NDISP_CE
3	G2	PD23	TCLK0	TimerCounter/TSAD3		BLDM	BLDM
2	F1	PD22	TIOA2	TimerCounter/TSAD2	BLDM0	BLDA	ID0
1	E1	PD21	TIOA1	TimerCounter/TSAD1	BLD	BLD	BLD
0	D2	PD20	TIOA0	TimerCounter/TSAD0	BLDM3		BLDRM

Figure 2: The ADC input pin usage for IQP, HDS, and FRC products.

To facilitate ADC input additions or removal with ease, the pin configuration for each build is an input parameter into the driver, defined as an 8 bit mask, with the bit ID corresponding to the respective Driver Pin ID. After the installation is complete, these input parameters are defined in file: /etc/insync/in_insync_adcc.sh as:

IQP_CHANNEL_MASK=0xF7	# 1111 0111 -> 7 adc input channels configured
HDS_CHANNEL_MASK=0x0E	# 0000 1110	-> only 3 adc input channels configured
FRC_CHANNEL_MASK=0xFF	# 1111 1111	-> all 8 adc input channels configured

If any changes are made to the ADC inputs please ensure that you accordingly set the correct mask in file /etc/insync/in_insync_adcc.sh.

The Control Pins

There are 2 other pins that need to be setup for the ADC to function.

TSADVREF Pin:

The highest possible voltage that can appear on the ADC input pins above must be applied to the TSADVREF pin (pin E2) prior to triggering the analogue to digital conversion. When triggerred, the ADC controller is configured to perform conversion on a full range between 0V and the reference voltage applied to TSADVREF.

TSADTRIG Pin:

After (a) the reference voltage (vRef) is applied to TSADVREF, and (b) the input voltages (vInput_x, x=0..7) are applied to one or more of the configured pins ( vInput_x <= vRef)) the conversion performance is triggered by setting the TSADTRIG pin from Low to High, on the rising edge. (If the logic on your board is set to active low, then change my code in the driver file to trigger conversion on the falling edge, and then you can trigger the ADC conversions by setting the TSADTRIG pin from High to Low.)

Conversion

On detecting the Low -> High rising edge, the ADC controller will serially (one after the other) perform analogue to digital conversion going from Pin ID 0 to Pin ID 7 respectively.

The result of each conversion is a 10 bit value stored in Channel Data Register [0...7] corresponding to the respective pin.

Thus a voltage equal to the voltage on TSADVREF will convert to 1023; 0V will convert to 0; and a voltage on the input pin withing the voltage range will convert to a corresponding value between 0 and 1023.

Input Events

After the completion of each conversion on each pin, the controller is configured to trigger an EOC (End Of Conversion) interrupt, which my Driver catches and services via its main Interrupt Service Routine.

Upon catching the EOC interrupt for each channel:
- The Driver will read the 10 bit ADC reading from the corresponding pins CDR (Channel Data Register)
- It will shift this 10 bit reading 3 bits to the left ( << 3 )
- It will store the 3 bit (0-7) Driver Pin ID to which the reading corresponds to in the 3 least significant bits
- And then send the resulting 13 bit value as an ABS_Y event up to the user space.

The input event driver will send the events up only when it receives a SYNC event signal from my device driver below it. Hence, for each ADC input one would receive 2 events into the user space:
- An ABS_Y event ( type = 3, code = 1, value = <13 bit value>),
- Followed by a SYNC signal ( type = 0, code = 0, value = 0 )

eg:
[product@Monk vadcc]$ dmesg | fgrep input13
[ 7876.088211] evbug.c: Event. Dev: input13, Type: 3, Code: 1, Value: 673
[ 7876.088216] evbug.c: Event. Dev: input13, Type: 0, Code: 0, Value: 0
[ 7877.087998] evbug.c: Event. Dev: input13, Type: 3, Code: 1, Value: 2117
[ 7877.088003] evbug.c: Event. Dev: input13, Type: 0, Code: 0, Value: 0
[ 7878.087778] evbug.c: Event. Dev: input13, Type: 3, Code: 1, Value: 6014
[ 7878.087783] evbug.c: Event. Dev: input13, Type: 0, Code: 0, Value: 0
[ 7879.087558] evbug.c: Event. Dev: input13, Type: 3, Code: 1, Value: 2531
[ 7879.087563] evbug.c: Event. Dev: input13, Type: 0, Code: 0, Value: 0
[ 7880.087338] evbug.c: Event. Dev: input13, Type: 3, Code: 1, Value: 85
[ 7880.087342] evbug.c: Event. Dev: input13, Type: 0, Code: 0, Value: 0

Note: If N out of 8 pins are configured as defined by the Input Pin Mask in file /etc/insync/in_insync_adcc.sh, then each time the TSADTRIG pins is sent high, N conversions are performed, in the order of the pin IDs, and N pairs of input events (an ABS_Y and SYNC event each) are sent up to the user-space.

ADC Input Events in the User Space

The ADC events are captured in the user space via the driver event device node in /etc/input/eventX. This X is variable as the driver will grab the next event ID not already used by another driver.

To identify the input event interface for the ADC driver, my driver is programmed to put a permanent symbolic link to the right event node from:
/dev/input/by-path/platform-insync_adcc-event

which your application can always lock as a constant device.

The events are read from this dev node into an input event structure defined in /usr/include/linux/input.h:

/*
 * The event structure itself
 */

struct input_event
{
    struct timeval time;
    __u16 type;
    __u16 code;
    __s32 value;
};

The Installation Guide

3.1.	Save and unzip the archive provided.

$ su – bitbake
$ gunzip adc.tar.gz
$ tar -xvf adc.tar

 The following files are provided for the installation of the complete Driver and and its	development and test tools.

The driver files:
insync_adcc.c	// the main driver source code to go in drivers/input/touchscreen/
in_insync_adcc.sh	// the Pin Mask parameter setting script to go
// into /etc/insync/ on the device
insync-dev.conf	// the Module loading modprobe configuration file to go
// into /etc/modprobe.d/ on the device

The development & test tool files:
vadcc.c	// the virtual simulator file to go in drivers/input/mouse/
Makefile.local	// the makefile to build the virtual simulator against the current
// running machine's kernel
in_vadcc.sh	// the Pin Mask parameter definition file for the virtual driver
// to go into /etc/insync/ in user-space
vadcc_data.c	// the user space program that generates data
// simulating ADC inputs for the virtual simulator

The Sample user-space controller to use as a template:
adc_test.c

Building the Drivers:

  1. Install the driver source and the simulator sorce into the kernel tree:

$ export KRN=<the kernel tree root>
$ cp ./adcc/insync_adcc.c $KRN/drivers/input/touchscreen/
$ cp ./adcc/vadcc.c $KRN/drivers/input/mouse/

  1. Edit the Kconfig files and add the following configurations to build the 2 drivers:

To $KRN/drivers/input/touchscreen/Kconfig add the highlighted block
within the “if INPUT_TOUCHSCREEN” block; please ensure that the architecture of the board in the depends clause is the correct one:

#
# Touchscreen driver configuration
#
menuconfig INPUT_TOUCHSCREEN
bool "Touchscreens"
help
  Say Y here, and a list of supported touchscreens will be displayed.
  This option doesn't affect the kernel.

  If unsure, say Y.

if INPUT_TOUCHSCREEN

config TOUCHSCREEN_INSYNC_ADCC
tristate "Insync ADC Interface"
depends on ARCH_AT91SAM9G45IQP
default m
help
  The Insync 8pin ADC controller will be compiled as a modules.

  To compile this driver as a module, choose M here: the
  module will be called insync_adcc.
...

Similarly add the highlighted block below to $KRN/drivers/input/mouse/Kconfig:

#
# Mouse driver configuration
#
menuconfig INPUT_MOUSE
bool "Mice"
default y
help
  Say Y here, and a list of supported mice will be displayed.
  This option doesn't affect the kernel.

  If unsure, say Y.

if INPUT_MOUSE

config VADCC
tristate "Virtual ADC driver"
default m
help
Virtual ADC driver emulator driven by user space inputs.

  1. Edit the Makefiles and add the following lines to build the 2 modules:

To $KRN/drivers/input/touchscreen/Makefile, add the line:

obj-$(CONFIG_TOUCHSCREEN_INSYNC_ADCC)	+= insync_adcc.o

Tp $KRN/drivers/input/mouse/Makefile, add the line:

obj-$(CONFIG_VADCC)	+= vadcc.o

  1. Edit the correct board source file and make sure to remove the Atmel touchscreen driver	which will conflict with the insync_adcc driver resulting in our driver failing to load:
$ vim $KRN/arch/arm/mach-at91/board-sam9g45iqp.c

Comment out the Atmel touchscreen driver loading in:
static void __init ek_board_init(void)
{
...
/* Touch Screen */
    // at91_add_device_tsadcc(&ek_tsadcc_data);
...
}

  1. Now from the kernel tree root run config:
$ cd $KRN
$ make ARCH=arm menuconfig

In Input Options set
(a) enable evdev to build with the kernel with “y”
(b) mark evbug to build as a module with “m”
(c) enable touchscreen building
(d) enable mouse building
Device Drivers --->
   Input device support --->
...
<*>	Event interface
<M>	Event debugging
...
[*]	Mice	--->
...
[*]	Touchscreens	--->

Descend further into the Touchscreens submenu and mark the new Insync ADC driver to build as a loadable module:
     Device Drivers --->
   Input device support --->
   [*] Touchscreens	--->
<M>	Insync ADC interface

Descend also into the Mice submenu and mark the new vitual driver simulator to build as a loadable module:
Device Drivers --->
Input device support --->
[*] Mice	--->
    <M> Virtual ADC driver

Save these configurations and exit menuconfig.

  1. Build the new kernel and the modules, and tftp boot your device from the new Uimage	kernel image.
$ cd $KRN
$ make ARCH=arm Uimage
$ make ARCH=arm modules

Installing the Driver on the Device

  1. There are 3 kernel lodable modules built that we are interested in, the second and the 3rd	being development and test tools:
$KRN/drivers/input/touchscreen/insync_adcc.ko
$KRN/drivers/input/mouse/vadcc.ko
$KRN/drivers/input/evbug.ko

Copy these and the following modprobe configuration scripts in may tarball into your nfs mount “soft”	directory that is accessible within the device.
insync-dev.conf
in_insync_adcc.sh
in_vadcc.sh

  1. Install the adc driver on the device driver directory:
$ cd /soft
$ su
# cp insync_adcc.ko /lib/modules/linux...
# chown root:root /lib/modules/linux.../insync_adcc.ko
# depmod

  1. Install the modprobe configuration files to pass in Pin Masks as module parameters:
# cp insync-dev.conf /etc/modprobe.d
# chown root:root /etc/modprobe.d/insync*
# cp in_insync_adcc.sh /etc/insync
# chown root:root /etc/insync/*
# chmod u+x /etc/insync/in_insync_adcc.sh

  1. Install the udev configurations to setup correct permissioning on the event dev nodes:

# vim /etc/udev/rules.d/xx-insync.rules

Add (cut and paste) the 2 lines:

KERNEL=="event[0-9]*", ATTRS{uniq}=="vadcc", GROUP="product", MODE="0644"
KERNEL=="event[0-9]*", ATTRS{uniq}=="insync_adcc", GROUP="product", MODE="0640"

  1. Now ensure that the bootloader is configured to tftp boot from the new kernel Uimage and reboot. The driver should load automatically on reboot.

The boot log and dmesg should log success. e.g:
[xxx] input: Insync ADC Controller as /devices/platform/insync_adcc/input/input2

Note: the above highlighted last input group number should change (increment) dynamically, every time you unload and reload the driver.

There should now be a constant dev-node symbolic link:
# ls -l /dev/input/by-path/platform-insync_adcc-event

There should be an event interface that the above symbolic link points to with correct permissionsing:
# ls -l /dev/input/event*

There should be a sysfs group:
# find /sys/devices/platform/insync_adcc

  1. Once the hardware circuit is set up, now the driver is ready for use.

  1. Ensure the above configuration files and the drivers are incorporated into the image that bitbake produces that the device will boot from.

4. Development & Test Tools

  1. Udev Admin: this is a test tool that can be used to monitor the behaviour of a device in user-	space and probe for information it exports to the user-space:

Open a seperate terminal into the device and run:
# udevadm monitor

On the main terminal reload the device, and view the device information on the tty:
# rmmod insync_adcc
# modprobe insync_adcc

  1. The Virtual ADC Simulator: The vadcc module is a virtual simulator that will behave	exactly like the insync_adcc driver within the kernel and into the user space. The difference	is, instead of getting its interrupts from the hardware, it gets interrupts and its data from a	Channel Data Register simulation file in its sysfs.

The previous process has already installed the configuration environment required for	vadcc. Ensure that both modprobe and udev scripts for vadcc are installed similarly.	Then, load the simulation driver manually.
# cd /soft
# insmod vadcc
# dmesg

In addition to devfs and sysfs filesystems exactly parallel to the original insync_adcc driver,	vadcc should have a Channel Data Register simulation file in sysfs, that simulates the 8	Channel Data Registers in the tsadcc controller:
# ls -l /sys/devices/platform/vadcc/ADC_CDR

Now you can simulate event interrupts by sending data in the form “<Pin ID>,<ADC	reading>” into the above file:
# export CDR=/sys/devices/platform/vadcc/ADC_CDR
# echo “5,662” > $CDR; echo “0,10” > $CDR; echo “7,0” > $CDR

These events will now appear through the virtual driver's /dev/input/eventX (or	/dev/input/by-path/platform-vadcc-event sym-link) interface through a process	exactly equivalent to the original insync_adcc driver.

This tool has been instrumental for me for designing, testing and fine-tuning the original	driver and the user-space template controller. This, coupled with the data generator in 4.4	below, should give you an invaluable tool for further developing and testing your user-space	controller program using the ADC driver.

  1. The evbug Event Debugger:

The event debugger floods the dmesg logs with a lot of event details from all event	interfaces in /dev/input/. Hence, before proceeding find out the current input group of the	loaded device's event interface:
# ls /sys/devices/platform/insync_adcc/input/
or
# ls /sys/devices/platform/vadcc/input/

Load evbug, trigger some events, and search dmesg:

root@Monk mouse]# ls /sys/devices/platform/vadcc/input/
input9/
[root@Monk mouse]# insmod ../evbug.ko
[root@Monk mouse]# export CDR=/sys/devices/platform/vadcc/ADCC_CDR
[root@Monk mouse]# echo "6,10" > $CDR; echo "2,555" > $CDR; echo "0,1023" > $CDR
[root@Monk mouse]# dmesg| fgrep input9
[13759.836670] evbug.c: Event. Dev: input9, Type: 3, Code: 1, Value: 86
[13759.836674] evbug.c: Event. Dev: input9, Type: 0, Code: 0, Value: 0
[13759.836765] evbug.c: Event. Dev: input9, Type: 3, Code: 1, Value: 4442
[13759.836768] evbug.c: Event. Dev: input9, Type: 0, Code: 0, Value: 0
[13759.836848] evbug.c: Event. Dev: input9, Type: 3, Code: 1, Value: 8184
[13759.836851] evbug.c: Event. Dev: input9, Type: 0, Code: 0, Value: 0
[root@Monk mouse]# rmmod evbug

    Remember to unload evbug after debugging as it floods the kernel logs with large volumes of	event data.

  1. The Virtual Data Generator: vadc_data.c is the a user space program that generates data into the virtual devices CDR simulator file. This is a user space program, and to cross compile it we need to extend the cross compilation toolset into user-space programming.

Assuming that your cross compilation toolset is in /usr/opt/Codesourcery/bin/ and the toolset extension is arm-none-linux-gnueabi- :

Either perform:
# cp /usr/opt/Codesourcery/bin/arm-none-linux-gnueabu-* /usr/local/bin
# export CROSS_COMPILE=arm-none-linux-gnueabi-

Or perform:
# echo “PATH=$PATH:/usr/opt/Codesourcery/bin” >> ~/.bashrc
# source ~/.bashrc
# export CROSS_COMPILE=arm-none-linux-gnueabi-

Now copy the code into a local work directory for C programs and compile.
# ${CROSS_COMPILE}gcc vadcc_data.c -o vadcc_data

And run the data generator while the vadcc simulator is loaded. It generates one datum every second, and you can change the rate by the first parameter which is the time in seconds after each datum.
# vadcc_data 2

You will see an event generated by the simulator every 2 seconds in evbug logs in dmesg.

  1. Development & Testing on a Machine:

The above toolset and the setup of the development environment in 4.4 allows one to do all your user-space controller development and detailed testing on a machine other than the device, and cross compiling the final result for the device.

NOTE: It is not recommended to do kernel development against a Server kernel. One could partition any development machine and put Linux on a partition, making it dual bootable.

To compile the virtual simulator against the current running kernel on the machine, use the included Makefile.local,ensuring that you first back up the kernel tree's Makefile, and restore it afterwards. You can change the name of the module in Makefile.local (e.g. to evbug from vadcc) and use it to compile any module in its module directory.

# cp Makefile.local $KRN/drivers/input/mouse/
# cd $KRN/drivers/input/mouse
# cp Makefile Makefile.bak
# cp makefile.local Makefile
# make
# cp Makefile.bak Makefile
# insmod vadcc.ko

The above will build vadcc.ko that you can load into the current kernel of the compiling machine by replacing “vadcc” in the makefile with “evbug”.

To build evdev:
# cp Makefile.local ..
# cd ..
# vim Makefile.local
  :1,$r/vadcc/evbug/g
# cp Makefile Makefile.bak
# cp Makefile.local Makefile
# make
# cp Makefile.bak Makefile
# insmod evbug.ko
# rmmod evbug.co

You can view the machine's kernel logs:
# tail -f /var/log/messges

Note: It is not recommended to do kernel development against a Server kernel.

5. The Sample Controller

The sample user-space Controller is included in the archive: adc_test.c

Compile it for the device using the same C-development environment set up as in 4.4.
# ${CROSS_COMPILE}gcc adc_test.c -o adc_test

- Load the compiled vadcc simulator into the kernel.
- Run the data generator vadcc_data.
- Then run the sample controller adc_test
- You will see events being captured and processed by the temeplate controller

Review the code and you will see how to lock the device event node, capture and read ABS_Y and SYNC input events, and to extract the Pin ID and the ADC reading from this. You can fill out the placeholder function to do whatever required with the reading.

Run program with no arguments to test the actual insync_adcc.ko driver.
Run it with a “ -v” switch to test against the virtual simulator.

[root@Monk vadcc]# ./adc_test -v
Device: /dev/input/by-path/platform-vadcc-event
init(): ADC event device /dev/input/by-path/platform-vadcc-event (Virtual ADC Controller) initialized
ADC ABS_Y event: type = 3, code = 1, value = 396
ADC SYNC event: type = 0, code = 0, value = 0
processing ADC reading for ADC 4: 49
--------------------------
ADC ABS_Y event: type = 3, code = 1, value = 5292
ADC SYNC event: type = 0, code = 0, value = 0
processing ADC reading for ADC 4: 661
--------------------------
ADC ABS_Y event: type = 3, code = 1, value = 1948
ADC SYNC event: type = 0, code = 0, value = 0
processing ADC reading for ADC 4: 243
--------------------------
ADC ABS_Y event: type = 3, code = 1, value = 31
ADC SYNC event: type = 0, code = 0, value = 0
processing ADC reading for ADC 7: 3
--------------------------
ADC ABS_Y event: type = 3, code = 1, value = 3450
ADC SYNC event: type = 0, code = 0, value = 0
processing ADC reading for ADC 2: 431
--------------------------
^Cexiting ... on signal [2]

Note that I'm catching and servicing the ^C and other interrupts so that the device is not left in a bad state.